## Slide 1: PMP TOP MODULE DIAGRAM
By Salman Aslam
2022-EE-123

## Slide 2: Top Module Diagram

## Slide 3: Inputs of Top Module
addr (32-bits): address of the memory region which we want to access
size (3-bits): accessing No. of bytes
Byte-->(001) = 1 byte
half word--> (010) = 2 bytes
word (100)--> = 4 bytes
Rest of the values are illegal
oper (2-bits): Operation to be carried out on memory address data
Read (00)
Write (01)
Execute (10)

## Slide 4: Inputs of Top Module
priv_mode (2-bits): The privilege mode, on which the processor is operating
Machine mode (00)
Supervisor mode (01)
User mode (10)
rw_addr: Selects which PMP register to read or write.
wr_en: when high, allows writing into the PMP registers.
rd_en: when high, allows reading data from PMP registers.
wdata: Data to be written into a PMP register

## Slide 5: Outputs of Top Module
permission (2-bits):
i) Access granted (00)
ii) Load access fault (01)
iii) Store access fault (10)
iv) Instruction access fault (11)
rdata:
Output read data from PMP_Registers when accessing the registers

## Slide 6: PMP Register
Outputs:
rdata
Inputs:
priv_mode
rw_addr
wr_en
rd_en
wdata

## Slide 8: PMP Check Block
By Muhammad Furrukh
2022-EE-111

## Slide 9: Inputs
addr (32-bits): address that needs to be accessed
size (3-bits): number of bytes we want to access
i) byte(001) = 1 byte
ii) half word (010) = 2 bytes
iii) word (100) = 4 bytes
Rest of the values are illegal

## Slide 10: Continued
3. oper (2-bits): Operation to be carried out on memory address data
i) Read (00)
ii) Write (01)
iii) Execute (10)
4. priv_mode (2-bits): The privilege mode, on which the processor is operating
i) Machine mode (00)
ii) Supervisor mode (01)
iii) User mode (10)
5. PMP address and configuration registers data (32-bits each)

## Slide 11: Output
Permission (2-bits):
i) Access granted (00)
ii) Load access fault (01)
iii) Store access fault (10)
iv) Instruction access fault (11)

## Slide 12: PMP Check Logic

## Slide 13: Breaking Logic: addr_checkN
Purpose:
Check whether the desired memory byte(s) lie in the Nth pmp entry, where 0 < N ≤ 15
Inputs:
addr (32-bits): Address we are checking
addrN (32-bits): Data from Nth pmp_addr register
addrN-1 (32-bits): Data from (N-1)th pmp_addr register
size (3-bits): Number of bytes we want to access

## Slide 14: Continued
AN (2-bits): Address mode configured for Nth pmp entry
i) OFF mode (00)
ii) TOR mode (01)
iii) NA4 mode (10)
iv) NAPOT mode (11)
Ouputs:
Out (1-bit):
Present in the given entry (1)
Absent in the given entry (0)

## Slide 15: Difference between addr_check0 and addr_checkN
No addrN-1 input
Because there is no entry before 0th entry
As a result, it contains TOR0 instead of TOR
Rest of the logic is same

## Slide 16: NAPOT Block
In NAPOT mode:
For addrN = yyyy...yy011...1
Number of bits before and including the first 0, on lsb side, determine size of protected region
Say, the number of these bits is n. Then size of region is 2^(n+3)
Base address will be yyy...yy000...0
NAPOT block computes the base address and the size of the region (offset), then use it to check if the desired memory block lies in this region

## Slide 17: Top of Range(TOR) Block
By Umair Ahmad
2022-EE-113

## Slide 18: Inputs and Outputs
Inputs:
addr (32-bit): Address that we want to access
addrN-1 (32-bit): Lower bound
addrN (32-bit): Upper bound
size (3-bit): Size we want to access 000 -> 1 byte 010 -> 2 bytes(Half word) 100 -> 4 bytes(Full word)
Output:
Out (1-bit):
0 -> Region not in TOR
1 -> Region in TOR

## Slide 19
Logic Implementation

## Slide 20: Inputs
Inputs:
addr (32-bit): Address that we want to access
addrN (32-bit): Upper bound
size (3-bit): Size we want to access 000 -> 1 byte 010 -> 2 bytes(Half word) 100 -> 4 bytes(Full word)
Output:
Out (1-bit):
0 -> Region not in TOR0
1 -> Region in TOR0

## Slide 21
Logic Implementation

## Slide 22: Inputs
Inputs:
addr (32-bit): Address that we want to access
addrN (32-bit): Upper bound
size (3-bit): Size we want to access 000 -> 1 byte 010 -> 2 bytes(Half word) 100 -> 4 bytes(Full word)
Output:
Out (1-bit):
0 -> Region not in TOR0
1 -> Region in TOR0

## Slide 23
Logic Implementation

## Slide 24: Implementation in System Verilog
By Muhammad Boota & Waleed Tariq
2022-EE-134 2022-EE-124

## Slide 25: Thank you